QUALITY CONTROL & ASSURANCE DESIGNER/INSTALLER OSS CHECKLIST

PROPERTY OWNER:  	  	PERMIT ID#:

SITE ADDRESS:  	    	City/Zip:

DESIGNER:  	    	PH #:

INSTALLER:		PH #:

| FINAL | SITE AUDIT PAPER AUDIT | Installer: | Designer: | CCPH: |
| --- | --- | --- | --- | --- |
| Line # | TANKS, PUMP CHAMBERS AND VAULTS: | Initial | Date | Initial | Date | Initial | Date |
| 1 | Level in all directions, leak-tested and passed |  |  |  |  |  |  |
|  | Sized per design |  |  |  |  |  |  |
|  | Riser/lids secured to tank, appear water/gas tight |  |  |  |  |  |  |
|  | Baffle(s)/outlet filter with handle as required |  |  |  |  |  |  |
|  | Check valve(s) / vacuum break(s) - as required |  |  |  |  |  |  |
|  | Control panel operational (no timer over-ride) |  |  |  |  |  |  |
|  | Elapsed time meter/dose counter if not H2O metered |  |  |  |  |  |  |
|  | Pump(s)/alarm(s) working per design spec. |  |  |  |  |  |  |
|  | Electrical hard-wired prior to designer inspection |  |  |  |  |  |  |
|  | Pump and alarm on separate circuits (tested) |  |  |  |  |  |  |
|  | DISPOSAL COMPONENT (ALL TYPES) |  |  |  |  |  |  |
|  | Approved location per design/reserve area intact |  |  |  |  |  |  |
|  | Monitoring ports installed and secured |  |  |  |  |  |  |
|  | Check valves accessible from surface |  |  |  |  |  |  |
|  | Cleanouts, valve box and end sweeps present |  |  |  |  |  |  |
|  | Pipes flushed (if pressurized) |  |  |  |  |  |  |
|  | Cover soil per design |  |  |  |  |  |  |
|  | Splash blocks / caps as required |  |  |  |  |  |  |
|  | DRAINFIELD (ALL TRENCH/BED/DRIP) TYPES)YPES)TINFIELD: |  |  |  |  |  |  |
| 2 | D-box level |  |  |  |  |  |  |
| 4 | Trenches level +/- 1/2”. Installer verified w/ laser. |  |  |  |  |  |  |
|  | Gravelless panel / drip tube type per design |  |  |  |  |  |  |
| 5 | Trench depth, width and OC per plan |  |  |  |  |  |  |
| 16 | Approved lateral/tube # & length per plan |  |  |  |  |  |  |
|  | ABOVE GROUND SYSTEMS |  |  |  |  |  |  |
|  | Soil moisture checked and okay |  |  |  |  |  |  |
|  | Ground prep per specifications |  |  |  |  |  |  |
|  | SAND SYSTEMS |  |  |  |  |  |  |
|  | SM or SF dimensions per design (H, W & L match) design) |  |  |  |  |  |  |
|  | Sand Cards provided, meets design/required sieve specifications |  |  |  |  |  |  |
|  | SF liner water tight & seamed per RS&G |  |  |  |  |  |  |
|  | PROPRIETARY SYSTEMS |  |  |  |  |  |  |
|  | Operating per manufacture specifications |  |  |  |  |  |  |
|  | Disinfection system operational |  |  |  |  |  |  |
|  | Effluent sampling port installed |  |  |  |  |  |  |
|  | GLENDON |  |  |  |  |  |  |
|  | Jute net and seeding |  |  |  |  |  |  |
|  | Vessels set within ½” of level |  |  |  |  |  |  |
|  | Timer set per manufacturer specifications |  |  |  |  |  |  |
|  | SUBSURFACE DRIP |  |  |  |  |  |  |
|  | Flush mechanism operational |  |  |  |  |  |  |
|  | Air relief valve(s) at high point(s) |  |  |  |  |  |  |
|  | Permit ID#: ________________________ | Installer: | Designer: | CCPH: |
|  | GENERAL | Initial | Date | Initial | Date | Initial | Date |
|  | Trench bottom & sidewalls not smeared |  |  |  |  |  |  |
|  | Old tank(s) legally abandoned |  |  |  |  |  |  |
|  | Pipes bedded (or will be w/ backfill) |  |  |  |  |  |  |
|  | Gravel / rock clean & per RS&Gs, Geotextile |  |  |  |  |  |  |
|  | Permit and approved design on site |  |  |  |  |  |  |
|  | Pipes encased under driveways |  |  |  |  |  |  |
|  | Water/sewer pipe crossing mitigations met |  |  |  |  |  |  |
|  | CCPH conditions on front of design met |  |  |  |  |  |  |

INSTALLER TO COMPLETE, DESIGNER TO VERIFY

GENERAL INFO:  (check all that apply)

SYSTEM COMPONENTS:

SPECIFICATIONS:

SETBACKS (list distance):                                                                                                                            TIMER SETTING HELP CENTER:

** Note all non-significant changes including: (1)Reserve & Initial SSAS swap (if same type of treatment & adjacent). (2) Tank or treatment vessel relocate that does not affect dose or pump requirements. (3) Gravelless chamber brand change (with appropriate length adjust).  (4) Drainrock for chambers with 40% length increase.  (5)Septic tank outlet baffle filter different from design.  NOTE: “Significant” changes must be submitted to and approved by CCPH.

I certify by initialing the applicable boxes that this OSS system has been installed according to the approved design and meets CCC 24.17, WAC 246-272A and applicable RS&Gs governing on-site wastewater systems as required by the approved design

Final Inspection by Certified Installer:		                                                                           Date:                                   .

Final Inspection by Designer: 		                                                                           Date:                                   .

Final Inspection by CCPH: 	      	                                                                     Date:_________________

RECORD DRAWING

DATE: __________________________

OSS TYPE:_______________________________________________			PERMIT ID#

PROPERTY ADDRESS / LOCATION:

PERMIT ISSUED TO:					                   		PHONE#

DESIGNER’S NAME:				                      			PHONE#

INSTALLER’S NAME:			                      				PHONE#

Note:  This is a permanent record.  Please use a straight edge to prepare an accurate detailed drawing of the constructed OSS system, drawn to scale.

OR locations triangulated, including the following required information:

- Location of all roads/driveways.

- Triangulate the location in feet and inches of all septic / pump tank lids and distribution boxes unless risers are installed to the surface and noted on the as-built. Please use a sidebar box instead of drawing lines through the OSS.  Label 2 permanent points as A and B.

- Triangulate both ends of all drainfield laterals unless observation ports are installed to the surface at both ends of each lateral.

- Show all surface water features, wells, buildings, waterlines, curtain drains, roof infiltration systems, etc. and their distances to the OSS. Identify the Reserve Area and 100% area with length and width dimensions.

OR  a to-scale designer CAD drawing, including the above required information.

(Designer Stamp Required)

INSTALLER’S SIGNATURE:	DATE:

FINAL INSPECTION BY DESIGNER:  	DATE:

-OR-

FINAL INSPECTION BY CCPH:	DATE:

# Text boxes

For Office Use Only

CLARK COUNTY PUBLIC HEALTH

1601 E. Fourth Plain Blvd. ( PO Box 9825

Vancouver, WA  98666-8825

(360) 397-8428 ( Fax (360) 397-8084

BLDG. INFO:           	RESIDENTIAL                    COMMERCIAL                    BEDROOMS(list)                    OTHER(list)                                                                                    .

TYPE OF SYSTEM: 	GRAVITY                     PUMP TO GRAVITY                     PRESSURE DISTRIBUTION                     SAND FILTER                    S AND MOUND              .

GRAVELESS                    SANDLINED TRENCH/BED                    DRIP                    PROPRIETARY(list)                                                                        .

SEPTIC TANK:	VOLUME:			     MANUFACTURER:			        	        MODEL#:	  	      .

PUMP CHAMBER:	VOLUME:			     MANUFACTURER:				        MODEL#:		      .

CHAMBERS OR DRIP TUBE:	MANUFACTURER:	                                   	MODEL#:			        TOTAL LENGTH:

EFFLUENT FILTER:  	MANUFACTURER:	  	MODEL#:			         LOCATION:

DISINFECTION:	MANUFACTURER:	    	MODEL#:		  	         LOCATION:

PUMP INFO:	MANUFACTURER:	    	MODEL#: 		                           HP:	                        VOLTS:                  .

CONTROL PANEL:	MANUFACTURER:	                                   	MODEL#:			         HR METER: (  Y  /  N  )    COUNTER?: (  Y  /  N  )

MAX. DAILY FLOW		  (GPD)      ORIFICE SIZE:                       TOTAL ORIFICE #:                       PUMP FLOW:                    (GPM)    SQT HT:                      .

TRENCH WIDTH:                     TRENCH DEPTH:                     ON CENTER:                      TIMER “ON”:           min (F)              (G or H)      TIMER “OFF”:                    hrs (I)

DOSE DRAWDOWN:                  IN  =                    GAL ( E )        DOSES/DAY:                         HIGH WATER ALARM FLOAT*:                         ON/OFF FLOAT*:                  .

(and works as intended)                       (and works as intended)

*Setting measured in inches from top of the concrete on tank to the float clamp on the float tree or bottom of the Aquaworx bell sensor

A  ÷  B  =                      =   C

C  x  D  =                      =  GPM

E  ÷  GPM  =       .          = ( F . G )

G  x  60  =   :                   =   H

A = Inches drawdown during pump run test

B = Duration of pump run test (Recommend 2 min)

C = Calculated inches of drawdown per minute

D = Pump chamber gallons/inch.  See design.

E = Required dose size (gallons).  See design.

F = Timer “ON” min

G = Timer “ON” 1/10 min

H = Timer “ON” seconds

I = Timer “OFF” time

TANKS TO:       	WELLS*:                       SURFACE WATER:                  .

DISPOSAL TO:	WELLS*:                       SURFACE WATER:                  .

( ATTEMPTED TO IDENTIFY ALL WELLS WITHIN 150’

COMMENTS**:

“ON” TIME:

- Use ( F . G ) for dial timers

- Use ( F : H ) for other timers

“OFF” TIME: (per design)

- I  =  24hr  ÷  # doses per day

A  =

B  =

D  =

E  =

For Office Use Only

CLARK COUNTY PUBLIC HEALTH

1601 E. Fourth Plain Blvd. ( PO Box 9825

Vancouver, WA  98666-8825

(360) 397-8428 ( Fax (360) 397-8084